## Slide 1: SensorML and Sensor Web Enablement
Dr. Mike Botts
Earth System Science Center NSSTC University of Alabama in Huntsville
mike.botts@nsstc.uah.edu

## Slide 2: SensorML Basics Overview of Concepts and Applications

## Slide 3: SensorML History - 1
NASA Interuse Experiment (UAH, JPL: ‘93–’96)
  Use of SPICE planetary navigation system for Earth Observation
  Initial Sensor description file developed by Bill Taber of JPL
Space Time Toolkit (UAH: ’95 - present)
  Originally utilized SPICE for geolocation
  Later developed light-weight JAVA-based geolocation system with hardwired sensor classes
  Being used to test prototype SensorML designs through the application of sensor model classes

## Slide 4: SensorML History - 2
April 1998 - Recommendation to CEOS: Interoperability of Multiple Space Agency Sensor Data from the Global Mapping Task Team – Bernried, Germany
Definition of Problem: There is an increasing realization by Earth observation scientists that data from space-borne sensors are not adequately nor easily georeferenced to meet their requirements. The consequence of this is that it is currently extremely difficult or impossible to combine data from different space-borne sensors or ground-based data. The first impediment is the lack of adequate, publicly available data on the spatial-temporal extents of data from space-borne sensors.
Recommendation: We, the CEOS Global Mapping Task Team, recommend that the space agencies seriously consider the production, storage, public access, and interoperability of adequate data for describing the dynamics and geometry of the sensor system. These data might include satellite position (ephemeris), satellite rotations (attitude), sensor model (dynamics, geometry, and calibration), relevant planet models, and spacecraft clock model. This data should be made available in real-time. There should also be an effort to provide publicly available software to ingest the above data using a common API. Any recommendations for the most appropriate propagation model should be adequate documented or algorithms provided.

## Slide 5: SensorML History - 3
CEOS Global Mapping Task Team – Boulder (Botts – Sept. 1998)
  Presents beginnings of a Sensor Description Format
  Task Team recommends consideration of XML
CEOS Global Mapping Task Team – Charlottesville (Botts – Sept. 1999)
  Presents the initial XML version of SensorML
NASA Advanced Information Systems Technology (AIST) Program – March 2000
  March 2000 - Botts proposal accepted to continue development and implementation of SensorML
  Dec 2000 – funding received

## Slide 6: SensorML History - 4
ISO TC 211, Project 19130 – Sensor and Data Model
  Dec 2000 - Liping Di (CEOS GMTT member) proposes and gets accepted Sensor Model standards study
  Botts asked to serve as Team Member (he hasn’t been much help so far)
OpenGIS Military Pilot Project (MPP1) – March 2001
  Botts accepted to participate with emphasis on Sensor Web enabling
OpenGIS Open Web Services (OWS1) – September 2001
  Botts accepted to participate in defining OGC Sensor Web standards and protocols
  SensorML both serving as a prototype model and undergoing significant extensions and modifications under activity … particularly for more robust support of in-situ sensors
  EPA sponsorship
OpenGIS OWS 1.2 – May 2002
  Continuation of SensorML development and incorporation into Sensor Web Enablement with emphasis on dynamic, remote sensing
  NIMA sponsorship

## Slide 7: OpenGIS Sensor Web Enablement Components
Observable – a phenomenon that can be observed and measured (referenced in an ObservablesDictionary)
Sensor – a device that observes and/or measures a phenomenon (SensorML)
Observed value (Observation/Measurement) – the value returned by or derived from a sensor observation (e.g. quantity, count, boolean, category, ordered category, position)
Sensor Collection Service – a service that provides observed values
Registries – provide discovery mechanism for sensors and observed values

## Slide 8: Scope of SensorML Support
Designed to support a wide range of sensors
  Including both dynamic and stationary platforms
  Including both in-situ and remote sensors
Examples:
  Stationary, in-situ – chemical “sniffer”, thermometer, gravity meter
  Stationary, remote – stream velocity profiler, atmospheric profiler, Doppler radar
  Dynamic, in-situ – aircraft mounted ozone “sniffer”, GPS unit, dropsonde
  Dynamic, remote – satellite radiometer, airborne camera, soldier-mounted video

## Slide 9: Use of SensorML for variety of sensor types

## Slide 10: Information Provided by SensorML
Observation characteristics
  Physical properties measured (e.g. radiometry, temperature, concentration, etc.)
  Quality characteristics (e.g. accuracy, precision)
  Response characteristics (e.g. spectral curve, temporal response, etc.)
Geometry Characteristics
  Size, shape, spatial weight function (e.g. point spread function) of individual samples
  Geometric and temporal characteristics of sample collections (e.g. scans or arrays)
Description and Documentation
  Overall information about the sensor
  History and reference information supporting the SensorML document

## Slide 11: SensorML Concepts
SensorML is an XML schema for defining the geometric, dynamic, and observational characteristics of a sensor
The purpose of the sensor description:
  (1) provide general sensor information in support of data discovery
  (2) support the processing and analysis of the sensor measurements
  (3) support the geolocation of the measured data.
  (4) provide performance characteristics (e.g. accuracy, threshold, etc.)
  (5) archive fundamental properties and assumptions regarding sensor
SensorML provides functional model for sensor, not detail description of hardware
SensorML separates the sensor from its associated platform(s) and target(s)

## Slide 12
Components Needed for Geolocation of Sensor Data

## Slide 13: Applications of SensorML and SensorWeb Technology
Coincident search for relevant data (i.e. data discovery)
On-demand processing of data products
Dynamic on-demand fusion of disparate sensor data (interuse)
Pre-mission planning
Real-time guidance and pointing (e.g. UAVs)
On-board applications
  Autonomous operation / target recognition
  SensorWeb communication of location and targets
  Direct transmission of data and processing information to remote sites

## Slide 14: Determination of Sensor Footprint with Time

## Slide 15: Intelligent Retrieval and Co-registration of Sensor Data

## Slide 16: Visual Fusion of Disparate Sensor Data

## Slide 17: SensorML Status Completed Task and Current SensorML

## Slide 18: Completed Tasks
COMPLETE:
Define the initial SensorML standard and evaluate robustness of design (03/01)
Complete initial documentation (06/01)
Tested SensorML conceptual design for geolocation within hardwired sensor classes in Space Time Toolkit (08/01)
Completed initial redesign of SensorML with several extensions and modifications (01/02)
  Redefined standard in XML schema (rather than DTD)
  Provided more robust support for description of observation properties
  More generalized support provided for in-situ sensors
  Added capabilities for making SensorML instance a “living document” of sensor history and modifications – established Action schemas for both sensor and document history
  Established Interoperability with OpenGIS standards, particularly Geographic Markup Language (GML), Sensor Collection Service (SCS), Observables, Sensor Registries
Documented redesigned standard [OGC IPR 02-026] (04/02)
Current SensorML design implemented and tested under OpenGIS OWS1 activities (03/02)

## Slide 19
Basic Sensor Schema

## Slide 20: “measures” property

## Slide 21
Platform Schema

## Slide 22: Frames and Oriented Position Schema
General Frame
GML Frame

## Slide 23: Sensor Description

## Slide 24: “describedBy” Property

## Slide 25
Document Metadata

## Slide 26
Sensor Response

## Slide 27
Radiation Response

## Slide 28: SensorML Status Ongoing Directions and Activities

## Slide 29: Support for Dynamic Remote Sensors
Original SensorML DTD definition focused entirely on the geometric and dynamic properties of remote sensors (e.g. scanners and imagers)
Irony: Current SensorML Schema is devoid of support for dynamic remote sensors
  Result of OpenGIS OWS1 initial focus on in-situ sensors
  Current version provides more generality and better support for response characteristics (sensitivity, accuracy, operational environment, etc.)
  Current schema better supports Frames and Sensor Collections which will be used for defining scanning and imaging properties
Major focus of next two months will be incorporation of previous scanning and frame camera models into new schema

## Slide 30: On-Going Activities and Scheduled Deliverables
ON-GOING:
Redesigning support for remote sensors (07/02)
  Redesigning sample geometry and sensor collection geometries using a Frame schema concept
    e.g. sample geometry frame related to sensor frame through static or dynamic scan geometry definition
    Sensor frame related to platform frame through static or dynamic mounting specifications
    Platform frame related to target world frame through dynamic or static coordinate transforms accounting for platform position and orientation
  Developing sensor application schemas for scanners, frame cameras, and profilers
  Developing schema for specification of radiation sensitivity characteristics
  Developing schema for specification of radiation source characteristics
Implement parsers and integrate into Space-Time Toolkit (STT) for testing (08/02)
Implement parsers and libraries for processing and geolocating data using SensorML (08/02)
Provide and test SensorML documents for wide range of EO sensors (12/02)
Provide wizard for creating SensorML documents (12/02)
Submit SensorML to OpenGIS and ISO TC211 for acceptance (09/02)

## Slide 31: Detailed Near-term Directions
Support for remote sensors within new schema
  Geometry and dynamics
  Bring in concepts previously developed in original SensorML for scanners
  Design models for frame camera, active sensors, etc.
Better support for Sensor Collections
Full support for mobile/dynamic platforms and sensors
More definitions for Quality and Precision
More specific ResponseTypes
Radiation spectral model (used for both radiation source and for instrument sensitivity characteristics)
More complete examples!

## Slide 32: SensorML: Fundamental Geometry Model for Remote Scanners

## Slide 33: SensorML Scanning Principals
Geometry and dynamics of scanners and profilers defined in terms of Sweep, Elevation, and Profile coordinates
Sweep is an angle parameter and is always about the Z (polar) axis, Elevation is an angle parameter and about the Y axis, Profile is a distance parameter measured from the sensor center
The “nesting” of Sweep, Elevation, and Profile elements defines the order of scanning
Conic and linear sensors can be distinguished simply by the orientation of the sensor “spheroid” relative to the target

## Slide 34: Basic Properties of Scan Geometry/Dynamics
Element Attributes
SWEEP/ELEVATION direction, axis
fixedAngle angleUnits, basis, value
startAngle angleUnits, basis, value
extentAngle angleUnits, basis, value
stepAngle angleUnits, expression, value
startTime timeUnits, basis, value
extentTime timeUnits, basis, value
stepTime timeUnits
repeatTime timeUnits
numberOfSamples
PROFILE direction
fixedDistance distanceUnits, basis, value
startAngle distanceUnits, basis, value
extentAngle distanceUnits, basis, value
stepAngle distanceUnits, expression, value
numberOfSamples

## Slide 35: Geometry for Different Scanners

## Slide 36: Relevant Web Addresses
SensorML
  http://www.opengis.org/ (don’t know what public location will be)
  http://vast.uah.edu/SensorML (not yet updated for new schema)
Space Time Toolkit
  http://vast.uah.edu/SpaceTimeToolkit